## Slide 1
Faculty of Science and Engineering
Zijie Zhang ([20721407])
Posture-Aware Hybrid Control for a Two-Wheeled Legged Robot
From Analytical Compensation to Bounded Residual Recovery
HopperTrex Kinodynamic Model & Perturbation Profile
Key Contributions
01
Posture-aware nominal control
Model posture-induced drift; shape references.
83.68% less drift · 94.44% lower speed peaks.
02
Targeted wheel–leg residuals
12.42% shorter recovery; leg masking reduces
the matched-baseline gain to 3.82%.
03
Operational boundary mapping
40 delay/noise conditions reveal where
learned corrections become fragile.
Core Dilemma: Wheeled-legged locomotion exhibits severe wheel-leg dynamic coupling—changing leg posture alters balance equilibria, while wheels simultaneously govern locomotion and posture.
Our Paradigm: Analytical models resolve predictable steady-state drift; bounded residual RL improves high-impulse transient recovery.
01 Nominal compensation & reference shaping
Chart: Station drift: −83.68%
| -7.9140027919641004E-2 | -4.0354653665737497E-2 | -1.5692794118340001E-3 | 3.7216094842069503E-2 | 7.6001469095972995E-2
Before h=0.3024 | 0.045167 | 0.015954 | -0.012894 | -0.041737 | -0.07051
Before h=0.3085 | 0.045472 | 0.016064 | -0.012312 | -0.041219 | -0.070469
Before h=0.3146 | 0.045883 | 0.016124 | -0.01235 | -0.041733 | -0.07045
Before h=0.3206 | 0.045523 | 0.016368 | -0.012369 | -0.041689 | -0.070818
Before h=0.3267 | 0.045278 | 0.016317 | -0.012773 | -0.042211 | -0.071028
After h=0.3024 | -0.0076298 | -0.0024558 | 0.0016048 | 0.0063251 | 0.011353
After h=0.3085 | -0.0077439 | -0.0024651 | 0.0020973 | 0.0069993 | 0.011589
After h=0.3146 | -0.0070896 | -0.0026815 | 0.0023673 | 0.0069161 | 0.011398
After h=0.3206 | -0.0071379 | -0.0024877 | 0.0015672 | 0.0069372 | 0.011227
After h=0.3267 | -0.0077213 | -0.0025435 | 0.0018619 | 0.0066145 | 0.011313
Chart: Speed peak: −94.44%
| Step | 0.5 s | 1.0 s | 2.0 s
Worst of 12 transitions | 0.99557 | 0.21916 | 0.085237 | 0.055334
Compensated
(Flat: -83.7%)
Uncompensated
(Drifting)
[Measured Trade-off] Command shaping suppresses velocity peaks by 94.44% at the designed cost of settling time (0.78 s → 1.74 s), reducing actuator shock before learning is applied.
Insight: Classical compensation resolves deterministic kinematics and drift, establishing a robust, non-strawman baseline.
02 Bounded residual learning & leg-channel ablation
State +
commands
Classical backbone
LQR · yaw FF · posture
Residual policy
Balance · yaw · 4 leg channels
Bounded authority
Clip → Mask → Scale
Compose
Nominal + residual
Wheels
Slew → velocity clip
Legs
Joint-position clip
Actuator / Robot
State Feedback (q, q̇, θ, θ̇)
Chart: Classical vs Hybrid
| Hybrid | Classical
Mean recovery time (s) | 0.88719 | 1.013
Chart: Leg-channel ablation
| Legs masked | Full residual
Gain vs matched baseline | 0.038215 | 0.12417
Predefined 10% target
Punchline: Full residual exceeds the 10% engineering target (12.42% faster recovery). Leg-channel ablation removes ~70% of the observed learning benefit: the gain falls to 3.82% with leg residuals masked, supporting wheel–leg coordination.
Simulation · one training seed · 128 events per arm · same checkpoint, evaluation-time masking · own matched baselines
03 Operational boundary: delay & noise
Recorded termination events · 40 conditions · shared scale 0–22
None
Encoder
MEMS IMU
MEMS IMU ×2
Classical
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
2
0
20
40
60
80
Hybrid
0
0
0
2
6
0
0
0
0
3
0
0
0
0
10
0
0
0
0
22
0
20
40
60
80
0
22
Delay (ms)
Deployment Specification: Zero termination events through 40 ms support a provisional ≤40 ms control latency budget. Higher delays expose residual fragility; validate this budget on hardware before physical deployment.
04 Simulation demo
Scan for Push-Recovery Demo
MuJoCo physics · Side-by-side comparison
Reproducible simulation workflow
Notes: Revision 3. Supplied illustration: C:/Users/Jack/Downloads/Annotated Robotic Rover Chassis.png. Label cleanup uses deterministic local interpolation; CoM is schematic, not a computed mass centroid. Diagram reflects Stage5 historical action interface. 40 ms is a simulation probe result, not a validated physical safety bound. Policy has no verified transient-only gate; legs-masked means residual masking, not disabling leg actuation. ~70% is (12.42-3.82)/12.42 = 69.2% of relative improvement across own matched baselines, not a direct causal decomposition. QR supplied by user; target https://qrco.de/bh2NyL, previously resolved to https://www.youtube.com/watch?v=dLVX1cyY2kQ. Source deck and data remain unchanged. DATA {"title":"Residual Reinforcement Learning on a Classical Control Backbone for a Two-Wheeled Legged Robot","status":"Rendered and verified first-review poster delivered; identity fields and video link intentionally pending.","historical_revision":"2fb98ee534cb66a51049feab4256a7c16c3e5d65","checkpoint":"48a053f0d1acaa799b105c20bce29d5f4a738da36fd9117d4bdf5f03f2c63937","recovery":[{"label":"Full residual","baseline_s":1.01296875,"candidate_s":0.8871875,"gain_percent":12.417090853000145},{"label":"Leg residuals masked","baseline_s":0.99765625,"candidate_s":0.95953125,"gain_percent":3.8214565387627353}],"shaping":[{"setting":"Step","peak_vx":0.9955744743347168,"settling":0.78375,"source":"posture_transition_qualification_seed1.json"},{"setting":"0.5 s","peak_vx":0.21916067600250244,"settling":0.47000000000000003,"source":"posture_transition_shaped_t05_seed1.json"},{"setting":"1.0 s","peak_vx":0.08523677289485931,"settling":0.8925,"source":"posture_transition_shaped_t10_seed1.json"},{"setting":"2.0 s","peak_vx":0.055334124714136124,"settling":1.7425,"source":"posture_transition_shaped_t20_seed1.json"}],"station_before":[{"height_rmse":0.00017385387036483735,"lin_x_abs_mean":0.04516676068305969,"mean_actual_lin_x":0.04516676068305969,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007941698655486107,"pitch_rate_abs_p99":0.1975330114364624,"pitch_rmse":0.0042284708470106125,"target_height":0.30244420501302,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00016950022836681455,"lin_x_abs_mean":0.016387034207582474,"mean_actual_lin_x":0.015953615307807922,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.0075715878047049046,"pitch_rate_abs_p99":0.2044893354177475,"pitch_rmse":0.004059132654219866,"target_height":0.30244420501302,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.0002190444793086499,"lin_x_abs_mean":0.013527041301131248,"mean_actual_lin_x":-0.012893886305391788,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007800807245075703,"pitch_rate_abs_p99":0.21737553179264069,"pitch_rmse":0.0042506493628025055,"target_height":0.30244420501302,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.00025124524836428463,"lin_x_abs_mean":0.041738223284482956,"mean_actual_lin_x":-0.04173743724822998,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008263783529400826,"pitch_rate_abs_p99":0.21111318469047546,"pitch_rmse":0.004379974212497473,"target_height":0.30244420501302,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00012361383414827287,"lin_x_abs_mean":0.07051040977239609,"mean_actual_lin_x":-0.07051040977239609,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008213899098336697,"pitch_rate_abs_p99":0.23708240687847137,"pitch_rmse":0.00420512305572629,"target_height":0.30244420501302,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0},{"height_rmse":0.00020439868967514485,"lin_x_abs_mean":0.04547234997153282,"mean_actual_lin_x":0.04547234997153282,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007408831734210253,"pitch_rate_abs_p99":0.1821223646402359,"pitch_rmse":0.003934911452233791,"target_height":0.30850143536142827,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.0002044815046247095,"lin_x_abs_mean":0.016463523730635643,"mean_actual_lin_x":0.01606411300599575,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007676324341446161,"pitch_rate_abs_p99":0.19183140993118286,"pitch_rmse":0.004113319795578718,"target_height":0.30850143536142827,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.0002807713462971151,"lin_x_abs_mean":0.013071474619209766,"mean_actual_lin_x":-0.012311792001128197,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.00834136176854372,"pitch_rate_abs_p99":0.21071505546569824,"pitch_rmse":0.004382982850074768,"target_height":0.30850143536142827,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.0003242002858314663,"lin_x_abs_mean":0.041218604892492294,"mean_actual_lin_x":-0.041218604892492294,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008125711232423782,"pitch_rate_abs_p99":0.2135004699230194,"pitch_rmse":0.004269670695066452,"target_height":0.30850143536142827,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00017513742204755545,"lin_x_abs_mean":0.07046852260828018,"mean_actual_lin_x":-0.07046852260828018,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007953270338475704,"pitch_rate_abs_p99":0.21340548992156982,"pitch_rmse":0.0040899720042943954,"target_height":0.30850143536142827,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0},{"height_rmse":0.00018234059098176658,"lin_x_abs_mean":0.04588314890861511,"mean_actual_lin_x":0.04588314890861511,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007326836697757244,"pitch_rate_abs_p99":0.18348178267478943,"pitch_rmse":0.0037384971510618925,"target_height":0.3145586657098365,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00019932020222768188,"lin_x_abs_mean":0.016416501253843307,"mean_actual_lin_x":0.016123753041028976,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007082863710820675,"pitch_rate_abs_p99":0.18997536599636078,"pitch_rmse":0.003805150045081973,"target_height":0.3145586657098365,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.00030643981881439686,"lin_x_abs_mean":0.012883249670267105,"mean_actual_lin_x":-0.012349874712526798,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.00778412027284503,"pitch_rate_abs_p99":0.19443291425704956,"pitch_rmse":0.004132171627134085,"target_height":0.3145586657098365,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.00039231308619491756,"lin_x_abs_mean":0.04173346981406212,"mean_actual_lin_x":-0.04173346981406212,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008038573898375034,"pitch_rate_abs_p99":0.2182641327381134,"pitch_rmse":0.004222610499709845,"target_height":0.3145586657098365,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00024297492927871644,"lin_x_abs_mean":0.07044978439807892,"mean_actual_lin_x":-0.07044978439807892,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007743865251541138,"pitch_rate_abs_p99":0.22858718037605286,"pitch_rmse":0.00405929796397686,"target_height":0.3145586657098365,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0},{"height_rmse":0.00011429170262999833,"lin_x_abs_mean":0.04552328586578369,"mean_actual_lin_x":0.04552328586578369,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.006947821006178856,"pitch_rate_abs_p99":0.17653749883174896,"pitch_rmse":0.0035983207635581493,"target_height":0.32061589605824475,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00015984063793439418,"lin_x_abs_mean":0.016651656478643417,"mean_actual_lin_x":0.016368433833122253,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007048408500850201,"pitch_rate_abs_p99":0.19500163197517395,"pitch_rmse":0.003707015188410878,"target_height":0.32061589605824475,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.0002975034003611654,"lin_x_abs_mean":0.012835723347961903,"mean_actual_lin_x":-0.012368792667984962,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007994560524821281,"pitch_rate_abs_p99":0.21461619436740875,"pitch_rmse":0.004130638670176268,"target_height":0.32061589605824475,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.0003847567131742835,"lin_x_abs_mean":0.04168872535228729,"mean_actual_lin_x":-0.04168872535228729,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008054209873080254,"pitch_rate_abs_p99":0.20985572040081024,"pitch_rmse":0.00416987668722868,"target_height":0.32061589605824475,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00027684008819051087,"lin_x_abs_mean":0.0708182081580162,"mean_actual_lin_x":-0.0708182081580162,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008592686615884304,"pitch_rate_abs_p99":0.21707859635353088,"pitch_rmse":0.004361956380307674,"target_height":0.32061589605824475,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0},{"height_rmse":0.00015256401093211025,"lin_x_abs_mean":0.04527759179472923,"mean_actual_lin_x":0.04527759179472923,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007391609717160463,"pitch_rate_abs_p99":0.19880294799804688,"pitch_rmse":0.0037242660764604807,"target_height":0.326673126406653,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00010641425615176558,"lin_x_abs_mean":0.0166200939565897,"mean_actual_lin_x":0.016317477449774742,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007474322337657213,"pitch_rate_abs_p99":0.19395294785499573,"pitch_rmse":0.0038800628390163183,"target_height":0.326673126406653,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.00023220789444167167,"lin_x_abs_mean":0.013193544931709766,"mean_actual_lin_x":-0.012772513553500175,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.006912520155310631,"pitch_rate_abs_p99":0.20353606343269348,"pitch_rmse":0.003761588828638196,"target_height":0.326673126406653,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.00033165805507451296,"lin_x_abs_mean":0.04221079498529434,"mean_actual_lin_x":-0.04221079498529434,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007439782842993736,"pitch_rate_abs_p99":0.2059984803199768,"pitch_rmse":0.0038227203767746687,"target_height":0.326673126406653,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00027032537036575377,"lin_x_abs_mean":0.07102835923433304,"mean_actual_lin_x":-0.07102835923433304,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007872702553868294,"pitch_rate_abs_p99":0.19918079674243927,"pitch_rmse":0.0039871130138635635,"target_height":0.326673126406653,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0}],"station_after":[{"height_rmse":0.00011422487295931205,"lin_x_abs_mean":0.009485120885074139,"mean_actual_lin_x":-0.007629805244505405,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.010666525922715664,"pitch_rate_abs_p99":0.19738774001598358,"pitch_rmse":0.005824975669384003,"target_height":0.30244420501302,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00017753987049218267,"lin_x_abs_mean":0.007060606963932514,"mean_actual_lin_x":-0.002455759095028043,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.00831653643399477,"pitch_rate_abs_p99":0.19310256838798523,"pitch_rmse":0.004381893202662468,"target_height":0.30244420501302,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.00020133302314206958,"lin_x_abs_mean":0.007019440643489361,"mean_actual_lin_x":0.001604776130989194,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008012312464416027,"pitch_rate_abs_p99":0.21166177093982697,"pitch_rmse":0.004190211184322834,"target_height":0.30244420501302,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.00015717488713562489,"lin_x_abs_mean":0.009027182124555111,"mean_actual_lin_x":0.006325125694274902,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.010737927630543709,"pitch_rate_abs_p99":0.22538073360919952,"pitch_rmse":0.0055274395272135735,"target_height":0.30244420501302,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00012926847557537258,"lin_x_abs_mean":0.01242983341217041,"mean_actual_lin_x":0.011353434063494205,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.012048491276800632,"pitch_rate_abs_p99":0.23213443160057068,"pitch_rmse":0.006944906897842884,"target_height":0.30244420501302,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0},{"height_rmse":0.00012568464444484562,"lin_x_abs_mean":0.009485222399234772,"mean_actual_lin_x":-0.007743856403976679,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.011004761792719364,"pitch_rate_abs_p99":0.19528062641620636,"pitch_rmse":0.006141350604593754,"target_height":0.30850143536142827,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00020549038890749216,"lin_x_abs_mean":0.00725272111594677,"mean_actual_lin_x":-0.002465086057782173,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008215098641812801,"pitch_rate_abs_p99":0.1966637820005417,"pitch_rmse":0.0043594371527433395,"target_height":0.30850143536142827,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.00026068216538988054,"lin_x_abs_mean":0.007244644686579704,"mean_actual_lin_x":0.0020972939673811197,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.0075866589322686195,"pitch_rate_abs_p99":0.20680899918079376,"pitch_rmse":0.004231896251440048,"target_height":0.30850143536142827,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.00021906426991336048,"lin_x_abs_mean":0.009111982770264149,"mean_actual_lin_x":0.006999333389103413,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.009786408394575119,"pitch_rate_abs_p99":0.2177172303199768,"pitch_rmse":0.005188972223550081,"target_height":0.30850143536142827,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00013491036952473223,"lin_x_abs_mean":0.01271043997257948,"mean_actual_lin_x":0.011589261703193188,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.011163453571498394,"pitch_rate_abs_p99":0.25299277901649475,"pitch_rmse":0.006489579100161791,"target_height":0.30850143536142827,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0},{"height_rmse":0.00010744819155661389,"lin_x_abs_mean":0.008638516999781132,"mean_actual_lin_x":-0.0070896209217607975,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.011002922430634499,"pitch_rate_abs_p99":0.19213919341564178,"pitch_rmse":0.006156035698950291,"target_height":0.3145586657098365,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00020254874834790826,"lin_x_abs_mean":0.006960600148886442,"mean_actual_lin_x":-0.0026815468445420265,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008341909386217594,"pitch_rate_abs_p99":0.20080962777137756,"pitch_rmse":0.0043068393133580685,"target_height":0.3145586657098365,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.00027750778826884925,"lin_x_abs_mean":0.0071690804325044155,"mean_actual_lin_x":0.002367328153923154,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007725246716290712,"pitch_rate_abs_p99":0.19581986963748932,"pitch_rmse":0.004219655878841877,"target_height":0.3145586657098365,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.0002904982538893819,"lin_x_abs_mean":0.008898716419935226,"mean_actual_lin_x":0.006916059646755457,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.009638802148401737,"pitch_rate_abs_p99":0.2054133117198944,"pitch_rmse":0.0051255011931061745,"target_height":0.3145586657098365,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00019373034592717886,"lin_x_abs_mean":0.0122893201187253,"mean_actual_lin_x":0.011398443952202797,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.010842766612768173,"pitch_rate_abs_p99":0.22365739941596985,"pitch_rmse":0.006231054197996855,"target_height":0.3145586657098365,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0},{"height_rmse":0.00011218861618544906,"lin_x_abs_mean":0.008709180168807507,"mean_actual_lin_x":-0.007137898821383715,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.010955187492072582,"pitch_rate_abs_p99":0.1973436176776886,"pitch_rmse":0.0061577362939715385,"target_height":0.32061589605824475,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00016890361439436674,"lin_x_abs_mean":0.0069791697897017,"mean_actual_lin_x":-0.0024877001997083426,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008550627157092094,"pitch_rate_abs_p99":0.19760197401046753,"pitch_rmse":0.004442795645445585,"target_height":0.32061589605824475,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.00026882870588451624,"lin_x_abs_mean":0.006823875475674868,"mean_actual_lin_x":0.0015672380104660988,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007626565173268318,"pitch_rate_abs_p99":0.2056138664484024,"pitch_rmse":0.003999816719442606,"target_height":0.32061589605824475,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.00028351243236102164,"lin_x_abs_mean":0.008918791078031063,"mean_actual_lin_x":0.006937229540199041,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.00932585820555687,"pitch_rate_abs_p99":0.20580443739891052,"pitch_rmse":0.005009614862501621,"target_height":0.32061589605824475,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00022225864813663065,"lin_x_abs_mean":0.012313591316342354,"mean_actual_lin_x":0.011227017268538475,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.011337549425661564,"pitch_rate_abs_p99":0.24478933215141296,"pitch_rmse":0.0066415490582585335,"target_height":0.32061589605824475,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0},{"height_rmse":0.0002104254817822948,"lin_x_abs_mean":0.009115445427596569,"mean_actual_lin_x":-0.007721322122961283,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.010264570824801922,"pitch_rate_abs_p99":0.18918564915657043,"pitch_rmse":0.0055488101206719875,"target_height":0.326673126406653,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00011169620847795159,"lin_x_abs_mean":0.006535099353641272,"mean_actual_lin_x":-0.0025435301940888166,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008128964342176914,"pitch_rate_abs_p99":0.1946735382080078,"pitch_rmse":0.004189266823232174,"target_height":0.326673126406653,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.0002033898636000231,"lin_x_abs_mean":0.006897625979036093,"mean_actual_lin_x":0.0018619117327034473,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007795293815433979,"pitch_rate_abs_p99":0.20958605408668518,"pitch_rmse":0.004247201606631279,"target_height":0.326673126406653,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.00024582105106674135,"lin_x_abs_mean":0.008536030538380146,"mean_actual_lin_x":0.0066144876182079315,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.009855748154222965,"pitch_rate_abs_p99":0.19476854801177979,"pitch_rmse":0.005127625539898872,"target_height":0.326673126406653,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.0002240820467704907,"lin_x_abs_mean":0.012142687104642391,"mean_actual_lin_x":0.011313319206237793,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.011474156752228737,"pitch_rate_abs_p99":0.20383119583129883,"pitch_rmse":0.00683866161853075,"target_height":0.326673126406653,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0}],"latency_cells":[{"delay_ms":0,"delay_steps":0,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.011043879203498363,"policy":"zero_residual","post_kick_lin_x_abs_max":0.1307574063539505,"recovery_time_s":0.1,"standing_abs_vx_mean":0.006987220607697964,"terminated_events":0,"tracking_abs_error_mean":0.00720513891428709,"tracking_abs_error_p95":0.01852722093462944},{"delay_ms":20,"delay_steps":1,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.012163268402218819,"policy":"zero_residual","post_kick_lin_x_abs_max":0.11997531354427338,"recovery_time_s":0.18,"standing_abs_vx_mean":0.007109735161066055,"terminated_events":0,"tracking_abs_error_mean":0.008248977363109589,"tracking_abs_error_p95":0.020016200840473175},{"delay_ms":40,"delay_steps":2,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.013558503240346909,"policy":"zero_residual","post_kick_lin_x_abs_max":0.12098667770624161,"recovery_time_s":0.26,"standing_abs_vx_mean":0.008761467412114143,"terminated_events":0,"tracking_abs_error_mean":0.008709645830094814,"tracking_abs_error_p95":0.021766146644949913},{"delay_ms":60,"delay_steps":3,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.017446143552660942,"policy":"zero_residual","post_kick_lin_x_abs_max":0.13287465274333954,"recovery_time_s":0.4,"standing_abs_vx_mean":0.010456238873302937,"terminated_events":0,"tracking_abs_error_mean":0.0116716418415308,"tracking_abs_error_p95":0.027849527075886726},{"delay_ms":80,"delay_steps":4,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.02760768122971058,"policy":"zero_residual","post_kick_lin_x_abs_max":0.1461997777223587,"recovery_time_s":0.92,"standing_abs_vx_mean":0.01839355006814003,"terminated_events":0,"tracking_abs_error_mean":0.020391298457980156,"tracking_abs_error_p95":0.04236597567796707},{"delay_ms":0,"delay_steps":0,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.010844380594789982,"policy":"zero_residual","post_kick_lin_x_abs_max":0.11990196257829666,"recovery_time_s":0.08,"standing_abs_vx_mean":0.006949808448553085,"terminated_events":0,"tracking_abs_error_mean":0.007256990298628807,"tracking_abs_error_p95":0.01863228529691696},{"delay_ms":20,"delay_steps":1,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.011869456619024277,"policy":"zero_residual","post_kick_lin_x_abs_max":0.12309412658214569,"recovery_time_s":0.18,"standing_abs_vx_mean":0.007007367443293333,"terminated_events":0,"tracking_abs_error_mean":0.007992643862962723,"tracking_abs_error_p95":0.020468534901738167},{"delay_ms":40,"delay_steps":2,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.013673351146280766,"policy":"zero_residual","post_kick_lin_x_abs_max":0.12961448729038239,"recovery_time_s":0.28,"standing_abs_vx_mean":0.00862827431410551,"terminated_events":0,"tracking_abs_error_mean":0.009000776335597038,"tracking_abs_error_p95":0.022732291370630264},{"delay_ms":60,"delay_steps":3,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.017853394150733948,"policy":"zero_residual","post_kick_lin_x_abs_max":0.1293426901102066,"recovery_time_s":0.3,"standing_abs_vx_mean":0.010524452663958073,"terminated_events":0,"tracking_abs_error_mean":0.012121072970330715,"tracking_abs_error_p95":0.02783133089542389},{"delay_ms":80,"delay_steps":4,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.028069453313946724,"policy":"zero_residual","post_kick_lin_x_abs_max":0.150909423828125,"recovery_time_s":1.26,"standing_abs_vx_mean":0.018602658063173294,"terminated_events":0,"tracking_abs_error_mean":0.02049054391682148,"tracking_abs_error_p95":0.0429089218378067},{"delay_ms":0,"delay_steps":0,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.01314107608050108,"policy":"zero_residual","post_kick_lin_x_abs_max":0.1414753943681717,"recovery_time_s":0.18,"standing_abs_vx_mean":0.014406519010663033,"terminated_events":0,"tracking_abs_error_mean":0.014303396455943584,"tracking_abs_error_p95":0.038086310029029846},{"delay_ms":20,"delay_steps":1,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.014085836708545685,"policy":"zero_residual","post_kick_lin_x_abs_max":0.12586554884910583,"recovery_time_s":0.22,"standing_abs_vx_mean":0.014244974590837955,"terminated_events":0,"tracking_abs_error_mean":0.014384638518095016,"tracking_abs_error_p95":0.03695063665509224},{"delay_ms":40,"delay_steps":2,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.01747898943722248,"policy":"zero_residual","post_kick_lin_x_abs_max":0.1387210190296173,"recovery_time_s":0.28,"standing_abs_vx_mean":0.015932835638523102,"terminated_events":0,"tracking_abs_error_mean":0.015655843541026115,"tracking_abs_error_p95":0.04021057114005089},{"delay_ms":60,"delay_steps":3,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.021695401519536972,"policy":"zero_residual","post_kick_lin_x_abs_max":0.14992760121822357,"recovery_time_s":0.44,"standing_abs_vx_mean":0.017228471115231514,"terminated_events":0,"tracking_abs_error_mean":0.017300719395279884,"tracking_abs_error_p95":0.04270332679152489},{"delay_ms":80,"delay_steps":4,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.03229844570159912,"policy":"zero_residual","post_kick_lin_x_abs_max":0.20006190240383148,"recovery_time_s":1.34,"standing_abs_vx_mean":0.02235904522240162,"terminated_events":1,"tracking_abs_error_mean":0.02192194014787674,"tracking_abs_error_p95":0.0547175295650959},{"delay_ms":0,"delay_steps":0,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.020785534754395485,"policy":"zero_residual","post_kick_lin_x_abs_max":0.1483522653579712,"recovery_time_s":0.34,"standing_abs_vx_mean":0.02334274724125862,"terminated_events":0,"tracking_abs_error_mean":0.02241542376577854,"tracking_abs_error_p95":0.054450251162052155},{"delay_ms":20,"delay_steps":1,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.02451029047369957,"policy":"zero_residual","post_kick_lin_x_abs_max":0.1624964475631714,"recovery_time_s":0.44,"standing_abs_vx_mean":0.025096632540225983,"terminated_events":0,"tracking_abs_error_mean":0.02479550987482071,"tracking_abs_error_p95":0.06114121526479721},{"delay_ms":40,"delay_steps":2,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.03026701882481575,"policy":"zero_residual","post_kick_lin_x_abs_max":0.1623184084892273,"recovery_time_s":0.56,"standing_abs_vx_mean":0.027675826102495193,"terminated_events":0,"tracking_abs_error_mean":0.02679629996418953,"tracking_abs_error_p95":0.06524382531642914},{"delay_ms":60,"delay_steps":3,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.038258396089076996,"policy":"zero_residual","post_kick_lin_x_abs_max":0.17828451097011566,"recovery_time_s":0.74,"standing_abs_vx_mean":0.0303372610360384,"terminated_events":0,"tracking_abs_error_mean":0.02987164817750454,"tracking_abs_error_p95":0.07334631681442261},{"delay_ms":80,"delay_steps":4,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.0708014965057373,"policy":"zero_residual","post_kick_lin_x_abs_max":0.2983553111553192,"recovery_time_s":3.58,"standing_abs_vx_mean":0.04753377288579941,"terminated_events":2,"tracking_abs_error_mean":0.04053782299160957,"tracking_abs_error_p95":0.10227109491825104},{"delay_ms":0,"delay_steps":0,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.011351809836924076,"policy":"candidate","post_kick_lin_x_abs_max":0.11191771924495697,"recovery_time_s":0.08,"standing_abs_vx_mean":0.006497347727417946,"terminated_events":0,"tracking_abs_error_mean":0.006531170569360256,"tracking_abs_error_p95":0.01671610213816166},{"delay_ms":20,"delay_steps":1,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.011603688821196556,"policy":"candidate","post_kick_lin_x_abs_max":0.14142851531505585,"recovery_time_s":0.22,"standing_abs_vx_mean":0.00858239084482193,"terminated_events":0,"tracking_abs_error_mean":0.008699791505932808,"tracking_abs_error_p95":0.021975353360176086},{"delay_ms":40,"delay_steps":2,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.013165956363081932,"policy":"candidate","post_kick_lin_x_abs_max":0.12976570427417755,"recovery_time_s":0.24,"standing_abs_vx_mean":0.009301927872002125,"terminated_events":0,"tracking_abs_error_mean":0.01005501952022314,"tracking_abs_error_p95":0.02599981613457203},{"delay_ms":60,"delay_steps":3,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.016171107068657875,"policy":"candidate","post_kick_lin_x_abs_max":0.132547527551651,"recovery_time_s":0.3,"standing_abs_vx_mean":0.010480305179953575,"terminated_events":2,"tracking_abs_error_mean":0.011140689253807068,"tracking_abs_error_p95":0.027021288871765137},{"delay_ms":80,"delay_steps":4,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.030529405921697617,"policy":"candidate","post_kick_lin_x_abs_max":0.2935265600681305,"recovery_time_s":2.1,"standing_abs_vx_mean":0.019155452027916908,"terminated_events":6,"tracking_abs_error_mean":0.020555447787046432,"tracking_abs_error_p95":0.04886236786842346},{"delay_ms":0,"delay_steps":0,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.011157880537211895,"policy":"candidate","post_kick_lin_x_abs_max":0.11497818678617477,"recovery_time_s":0.08,"standing_abs_vx_mean":0.006153447553515434,"terminated_events":0,"tracking_abs_error_mean":0.006454714108258486,"tracking_abs_error_p95":0.016684992238879204},{"delay_ms":20,"delay_steps":1,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.011300064623355865,"policy":"candidate","post_kick_lin_x_abs_max":0.12796908617019653,"recovery_time_s":0.16,"standing_abs_vx_mean":0.008384688757359982,"terminated_events":0,"tracking_abs_error_mean":0.008600873872637749,"tracking_abs_error_p95":0.022157354280352592},{"delay_ms":40,"delay_steps":2,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.013002783991396427,"policy":"candidate","post_kick_lin_x_abs_max":0.13947659730911255,"recovery_time_s":0.24,"standing_abs_vx_mean":0.009780127555131912,"terminated_events":0,"tracking_abs_error_mean":0.009976571425795555,"tracking_abs_error_p95":0.02580813691020012},{"delay_ms":60,"delay_steps":3,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.01647009328007698,"policy":"candidate","post_kick_lin_x_abs_max":0.13268159329891205,"recovery_time_s":0.36,"standing_abs_vx_mean":0.010261217132210732,"terminated_events":0,"tracking_abs_error_mean":0.011237612925469875,"tracking_abs_error_p95":0.027789568528532982},{"delay_ms":80,"delay_steps":4,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.02985461615025997,"policy":"candidate","post_kick_lin_x_abs_max":0.15648983418941498,"recovery_time_s":1.18,"standing_abs_vx_mean":0.02020798623561859,"terminated_events":3,"tracking_abs_error_mean":0.019325407221913338,"tracking_abs_error_p95":0.045518577098846436},{"delay_ms":0,"delay_steps":0,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.01311526820063591,"policy":"candidate","post_kick_lin_x_abs_max":0.11053044348955154,"recovery_time_s":0.1,"standing_abs_vx_mean":0.013527307659387589,"terminated_events":0,"tracking_abs_error_mean":0.013584049418568611,"tracking_abs_error_p95":0.03556500002741814},{"delay_ms":20,"delay_steps":1,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.015923790633678436,"policy":"candidate","post_kick_lin_x_abs_max":0.14582562446594238,"recovery_time_s":0.26,"standing_abs_vx_mean":0.016116809099912643,"terminated_events":0,"tracking_abs_error_mean":0.015706516802310944,"tracking_abs_error_p95":0.04001062363386154},{"delay_ms":40,"delay_steps":2,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.019215052947402,"policy":"candidate","post_kick_lin_x_abs_max":0.15189579129219055,"recovery_time_s":0.3,"standing_abs_vx_mean":0.016692815348505974,"terminated_events":0,"tracking_abs_error_mean":0.016871217638254166,"tracking_abs_error_p95":0.04197467118501663},{"delay_ms":60,"delay_steps":3,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.02352210506796837,"policy":"candidate","post_kick_lin_x_abs_max":0.1679765284061432,"recovery_time_s":0.52,"standing_abs_vx_mean":0.018342306837439537,"terminated_events":0,"tracking_abs_error_mean":0.018747352063655853,"tracking_abs_error_p95":0.0467117503285408},{"delay_ms":80,"delay_steps":4,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.0492582730948925,"policy":"candidate","post_kick_lin_x_abs_max":0.2198176383972168,"recovery_time_s":1.66,"standing_abs_vx_mean":0.0349641889333725,"terminated_events":10,"tracking_abs_error_mean":0.028445031493902206,"tracking_abs_error_p95":0.07210559397935867},{"delay_ms":0,"delay_steps":0,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.020040947943925858,"policy":"candidate","post_kick_lin_x_abs_max":0.14655670523643494,"recovery_time_s":0.14,"standing_abs_vx_mean":0.022375021129846573,"terminated_events":0,"tracking_abs_error_mean":0.022285910323262215,"tracking_abs_error_p95":0.053159549832344055},{"delay_ms":20,"delay_steps":1,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.026711465790867805,"policy":"candidate","post_kick_lin_x_abs_max":0.157490074634552,"recovery_time_s":0.36,"standing_abs_vx_mean":0.025624293833971024,"terminated_events":0,"tracking_abs_error_mean":0.025862382724881172,"tracking_abs_error_p95":0.06469564884901047},{"delay_ms":40,"delay_steps":2,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.03461362048983574,"policy":"candidate","post_kick_lin_x_abs_max":0.20025943219661713,"recovery_time_s":0.56,"standing_abs_vx_mean":0.029068009927868843,"terminated_events":0,"tracking_abs_error_mean":0.02860417775809765,"tracking_abs_error_p95":0.07147517055273056},{"delay_ms":60,"delay_steps":3,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.043304260820150375,"policy":"candidate","post_kick_lin_x_abs_max":0.1822700798511505,"recovery_time_s":0.62,"standing_abs_vx_mean":0.0323825441300869,"terminated_events":0,"tracking_abs_error_mean":0.03217266872525215,"tracking_abs_error_p95":0.07953979820013046},{"delay_ms":80,"delay_steps":4,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.12649685144424438,"policy":"candidate","post_kick_lin_x_abs_max":1.6340394020080566,"recovery_time_s":5.04,"standing_abs_vx_mean":0.07934746146202087,"terminated_events":22,"tracking_abs_error_mean":0.06326030939817429,"tracking_abs_error_p95":0.16573189198970795}],"interface":{"policy":"clip(raw, -1, 1) -> mask -> scale","wheels":"classical + mapped balance/yaw residual -> slew limit -> velocity clip","legs":"posture map + four leg residuals -> soft joint-position clip -> encoder bias correction","outputs":["2 wheel velocity targets (rad/s)","4 leg position targets (rad)"],"posture_reference":"height/pitch slew is upstream; no separate final leg slew in this historical action implementation"}}

## Slide 2
Faculty of Science and Engineering
Zijie Zhang (20721407)
Posture-Aware Hybrid Control for a Two-Wheeled Legged Robot
From Analytical Compensation to Bounded Residual Recovery
HopperTrex Kinodynamic Model & Perturbation Profile
Key Results at a Glance
01
84% less drift
Physics-based compensation cancels posture drift;
command shaping cuts speed peaks by 94%.
02
12% faster push recovery
Learned wheel–leg corrections; masking the leg
channels drops the gain to 3.8%.
03
≤40 ms safe latency budget
Zero failures up to 40 ms across 40 delay/noise
tests; learned corrections turn fragile beyond.
The Problem: Changing leg posture shifts the robot's balance point, while the same wheels must both drive and balance—so legs and wheels are tightly coupled.
Our Approach: A physics model removes predictable drift; a bounded learned policy adds fast recovery from sudden pushes.
01 Nominal compensation & reference shaping
Chart: Station drift: −83.68%
| -7.9140027919641004E-2 | -4.0354653665737497E-2 | -1.5692794118340001E-3 | 3.7216094842069503E-2 | 7.6001469095972995E-2
Before h=0.3024 | 0.045167 | 0.015954 | -0.012894 | -0.041737 | -0.07051
Before h=0.3085 | 0.045472 | 0.016064 | -0.012312 | -0.041219 | -0.070469
Before h=0.3146 | 0.045883 | 0.016124 | -0.01235 | -0.041733 | -0.07045
Before h=0.3206 | 0.045523 | 0.016368 | -0.012369 | -0.041689 | -0.070818
Before h=0.3267 | 0.045278 | 0.016317 | -0.012773 | -0.042211 | -0.071028
After h=0.3024 | -0.0076298 | -0.0024558 | 0.0016048 | 0.0063251 | 0.011353
After h=0.3085 | -0.0077439 | -0.0024651 | 0.0020973 | 0.0069993 | 0.011589
After h=0.3146 | -0.0070896 | -0.0026815 | 0.0023673 | 0.0069161 | 0.011398
After h=0.3206 | -0.0071379 | -0.0024877 | 0.0015672 | 0.0069372 | 0.011227
After h=0.3267 | -0.0077213 | -0.0025435 | 0.0018619 | 0.0066145 | 0.011313
Chart: Speed peak: −94.44%
| Step (unshaped) | 0.5 s | 1.0 s | 2.0 s
Worst of 12 transitions | 0.99557 | 0.21916 | 0.085237 | 0.055334
Compensated
(−83.68%)
Uncompensated
(Drifting)
Trade-off: Command shaping suppresses velocity peaks by 94.44% at the designed cost of settling time (0.78 s → 1.74 s), reducing actuator shock before learning is applied.
Insight: Classical compensation removes predictable drift, giving a strong baseline before any learning is added.
02 Bounded residual learning & leg-channel ablation
State +
commands
Classical backbone
LQR · yaw FF · posture
Residual policy
Balance · yaw · 4 leg channels
Bounded authority
Clip → Mask → Scale
Compose
Nominal + residual
Wheels
Speed limit
Legs
Position limit
Actuator / Robot
State Feedback (q, q̇, θ, θ̇)
Chart: Classical vs Hybrid (lower is better)
| Hybrid | Classical
Mean recovery time (s) | 0.88719 | 1.013
Chart: Leg-channel ablation
| Legs masked | Full residual
Gain vs matched baseline | 0.038215 | 0.12417
↓ Predefined 10% target
Key Result: Full residual beats the 10% target (12.42% faster recovery). Masking leg residuals removes ~70% of the learning benefit: the gain falls to 3.82%, showing wheel–leg coordination matters.
Simulation · one training seed · 128 events per arm · same checkpoint, evaluation-time masking · own matched baselines
03 Operational boundary: delay & noise
Termination events (lower is better) · dashed box = ≤40 ms safe zone · scale 0–22
None
Encoder
MEMS IMU
MEMS IMU ×2
Classical
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
2
0
20
40
60
80
Hybrid
0
0
0
2
6
0
0
0
0
3
0
0
0
0
10
0
0
0
0
22
0
20
40
60
80
0
22
Delay (ms)
Takeaway: Zero termination events up to 40 ms support a provisional ≤40 ms control latency budget. Beyond that, learned corrections become fragile—hardware validation is the next step.
04 Simulation demo
Scan for Push-Recovery Demo
MuJoCo physics · Side-by-side comparison
Reproducible simulation workflow
References: Johannink et al., ICRA 2019 · Schulman et al., PPO 2017
Failures
Notes: Revision 3. Supplied illustration: C:/Users/Jack/Downloads/Annotated Robotic Rover Chassis.png. Label cleanup uses deterministic local interpolation; CoM is schematic, not a computed mass centroid. Diagram reflects Stage5 historical action interface. 40 ms is a simulation probe result, not a validated physical safety bound. Policy has no verified transient-only gate; legs-masked means residual masking, not disabling leg actuation. ~70% is (12.42-3.82)/12.42 = 69.2% of relative improvement across own matched baselines, not a direct causal decomposition. QR supplied by user; target https://qrco.de/bh2NyL, previously resolved to https://www.youtube.com/watch?v=dLVX1cyY2kQ. Source deck and data remain unchanged. DATA {"title":"Residual Reinforcement Learning on a Classical Control Backbone for a Two-Wheeled Legged Robot","status":"Rendered and verified first-review poster delivered; identity fields and video link intentionally pending.","historical_revision":"2fb98ee534cb66a51049feab4256a7c16c3e5d65","checkpoint":"48a053f0d1acaa799b105c20bce29d5f4a738da36fd9117d4bdf5f03f2c63937","recovery":[{"label":"Full residual","baseline_s":1.01296875,"candidate_s":0.8871875,"gain_percent":12.417090853000145},{"label":"Leg residuals masked","baseline_s":0.99765625,"candidate_s":0.95953125,"gain_percent":3.8214565387627353}],"shaping":[{"setting":"Step","peak_vx":0.9955744743347168,"settling":0.78375,"source":"posture_transition_qualification_seed1.json"},{"setting":"0.5 s","peak_vx":0.21916067600250244,"settling":0.47000000000000003,"source":"posture_transition_shaped_t05_seed1.json"},{"setting":"1.0 s","peak_vx":0.08523677289485931,"settling":0.8925,"source":"posture_transition_shaped_t10_seed1.json"},{"setting":"2.0 s","peak_vx":0.055334124714136124,"settling":1.7425,"source":"posture_transition_shaped_t20_seed1.json"}],"station_before":[{"height_rmse":0.00017385387036483735,"lin_x_abs_mean":0.04516676068305969,"mean_actual_lin_x":0.04516676068305969,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007941698655486107,"pitch_rate_abs_p99":0.1975330114364624,"pitch_rmse":0.0042284708470106125,"target_height":0.30244420501302,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00016950022836681455,"lin_x_abs_mean":0.016387034207582474,"mean_actual_lin_x":0.015953615307807922,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.0075715878047049046,"pitch_rate_abs_p99":0.2044893354177475,"pitch_rmse":0.004059132654219866,"target_height":0.30244420501302,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.0002190444793086499,"lin_x_abs_mean":0.013527041301131248,"mean_actual_lin_x":-0.012893886305391788,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007800807245075703,"pitch_rate_abs_p99":0.21737553179264069,"pitch_rmse":0.0042506493628025055,"target_height":0.30244420501302,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.00025124524836428463,"lin_x_abs_mean":0.041738223284482956,"mean_actual_lin_x":-0.04173743724822998,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008263783529400826,"pitch_rate_abs_p99":0.21111318469047546,"pitch_rmse":0.004379974212497473,"target_height":0.30244420501302,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00012361383414827287,"lin_x_abs_mean":0.07051040977239609,"mean_actual_lin_x":-0.07051040977239609,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008213899098336697,"pitch_rate_abs_p99":0.23708240687847137,"pitch_rmse":0.00420512305572629,"target_height":0.30244420501302,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0},{"height_rmse":0.00020439868967514485,"lin_x_abs_mean":0.04547234997153282,"mean_actual_lin_x":0.04547234997153282,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007408831734210253,"pitch_rate_abs_p99":0.1821223646402359,"pitch_rmse":0.003934911452233791,"target_height":0.30850143536142827,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.0002044815046247095,"lin_x_abs_mean":0.016463523730635643,"mean_actual_lin_x":0.01606411300599575,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007676324341446161,"pitch_rate_abs_p99":0.19183140993118286,"pitch_rmse":0.004113319795578718,"target_height":0.30850143536142827,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.0002807713462971151,"lin_x_abs_mean":0.013071474619209766,"mean_actual_lin_x":-0.012311792001128197,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.00834136176854372,"pitch_rate_abs_p99":0.21071505546569824,"pitch_rmse":0.004382982850074768,"target_height":0.30850143536142827,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.0003242002858314663,"lin_x_abs_mean":0.041218604892492294,"mean_actual_lin_x":-0.041218604892492294,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008125711232423782,"pitch_rate_abs_p99":0.2135004699230194,"pitch_rmse":0.004269670695066452,"target_height":0.30850143536142827,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00017513742204755545,"lin_x_abs_mean":0.07046852260828018,"mean_actual_lin_x":-0.07046852260828018,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007953270338475704,"pitch_rate_abs_p99":0.21340548992156982,"pitch_rmse":0.0040899720042943954,"target_height":0.30850143536142827,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0},{"height_rmse":0.00018234059098176658,"lin_x_abs_mean":0.04588314890861511,"mean_actual_lin_x":0.04588314890861511,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007326836697757244,"pitch_rate_abs_p99":0.18348178267478943,"pitch_rmse":0.0037384971510618925,"target_height":0.3145586657098365,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00019932020222768188,"lin_x_abs_mean":0.016416501253843307,"mean_actual_lin_x":0.016123753041028976,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007082863710820675,"pitch_rate_abs_p99":0.18997536599636078,"pitch_rmse":0.003805150045081973,"target_height":0.3145586657098365,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.00030643981881439686,"lin_x_abs_mean":0.012883249670267105,"mean_actual_lin_x":-0.012349874712526798,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.00778412027284503,"pitch_rate_abs_p99":0.19443291425704956,"pitch_rmse":0.004132171627134085,"target_height":0.3145586657098365,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.00039231308619491756,"lin_x_abs_mean":0.04173346981406212,"mean_actual_lin_x":-0.04173346981406212,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008038573898375034,"pitch_rate_abs_p99":0.2182641327381134,"pitch_rmse":0.004222610499709845,"target_height":0.3145586657098365,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00024297492927871644,"lin_x_abs_mean":0.07044978439807892,"mean_actual_lin_x":-0.07044978439807892,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007743865251541138,"pitch_rate_abs_p99":0.22858718037605286,"pitch_rmse":0.00405929796397686,"target_height":0.3145586657098365,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0},{"height_rmse":0.00011429170262999833,"lin_x_abs_mean":0.04552328586578369,"mean_actual_lin_x":0.04552328586578369,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.006947821006178856,"pitch_rate_abs_p99":0.17653749883174896,"pitch_rmse":0.0035983207635581493,"target_height":0.32061589605824475,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00015984063793439418,"lin_x_abs_mean":0.016651656478643417,"mean_actual_lin_x":0.016368433833122253,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007048408500850201,"pitch_rate_abs_p99":0.19500163197517395,"pitch_rmse":0.003707015188410878,"target_height":0.32061589605824475,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.0002975034003611654,"lin_x_abs_mean":0.012835723347961903,"mean_actual_lin_x":-0.012368792667984962,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007994560524821281,"pitch_rate_abs_p99":0.21461619436740875,"pitch_rmse":0.004130638670176268,"target_height":0.32061589605824475,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.0003847567131742835,"lin_x_abs_mean":0.04168872535228729,"mean_actual_lin_x":-0.04168872535228729,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008054209873080254,"pitch_rate_abs_p99":0.20985572040081024,"pitch_rmse":0.00416987668722868,"target_height":0.32061589605824475,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00027684008819051087,"lin_x_abs_mean":0.0708182081580162,"mean_actual_lin_x":-0.0708182081580162,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008592686615884304,"pitch_rate_abs_p99":0.21707859635353088,"pitch_rmse":0.004361956380307674,"target_height":0.32061589605824475,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0},{"height_rmse":0.00015256401093211025,"lin_x_abs_mean":0.04527759179472923,"mean_actual_lin_x":0.04527759179472923,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007391609717160463,"pitch_rate_abs_p99":0.19880294799804688,"pitch_rmse":0.0037242660764604807,"target_height":0.326673126406653,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00010641425615176558,"lin_x_abs_mean":0.0166200939565897,"mean_actual_lin_x":0.016317477449774742,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007474322337657213,"pitch_rate_abs_p99":0.19395294785499573,"pitch_rmse":0.0038800628390163183,"target_height":0.326673126406653,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.00023220789444167167,"lin_x_abs_mean":0.013193544931709766,"mean_actual_lin_x":-0.012772513553500175,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.006912520155310631,"pitch_rate_abs_p99":0.20353606343269348,"pitch_rmse":0.003761588828638196,"target_height":0.326673126406653,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.00033165805507451296,"lin_x_abs_mean":0.04221079498529434,"mean_actual_lin_x":-0.04221079498529434,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007439782842993736,"pitch_rate_abs_p99":0.2059984803199768,"pitch_rmse":0.0038227203767746687,"target_height":0.326673126406653,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00027032537036575377,"lin_x_abs_mean":0.07102835923433304,"mean_actual_lin_x":-0.07102835923433304,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007872702553868294,"pitch_rate_abs_p99":0.19918079674243927,"pitch_rmse":0.0039871130138635635,"target_height":0.326673126406653,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0}],"station_after":[{"height_rmse":0.00011422487295931205,"lin_x_abs_mean":0.009485120885074139,"mean_actual_lin_x":-0.007629805244505405,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.010666525922715664,"pitch_rate_abs_p99":0.19738774001598358,"pitch_rmse":0.005824975669384003,"target_height":0.30244420501302,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00017753987049218267,"lin_x_abs_mean":0.007060606963932514,"mean_actual_lin_x":-0.002455759095028043,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.00831653643399477,"pitch_rate_abs_p99":0.19310256838798523,"pitch_rmse":0.004381893202662468,"target_height":0.30244420501302,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.00020133302314206958,"lin_x_abs_mean":0.007019440643489361,"mean_actual_lin_x":0.001604776130989194,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008012312464416027,"pitch_rate_abs_p99":0.21166177093982697,"pitch_rmse":0.004190211184322834,"target_height":0.30244420501302,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.00015717488713562489,"lin_x_abs_mean":0.009027182124555111,"mean_actual_lin_x":0.006325125694274902,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.010737927630543709,"pitch_rate_abs_p99":0.22538073360919952,"pitch_rmse":0.0055274395272135735,"target_height":0.30244420501302,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00012926847557537258,"lin_x_abs_mean":0.01242983341217041,"mean_actual_lin_x":0.011353434063494205,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.012048491276800632,"pitch_rate_abs_p99":0.23213443160057068,"pitch_rmse":0.006944906897842884,"target_height":0.30244420501302,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0},{"height_rmse":0.00012568464444484562,"lin_x_abs_mean":0.009485222399234772,"mean_actual_lin_x":-0.007743856403976679,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.011004761792719364,"pitch_rate_abs_p99":0.19528062641620636,"pitch_rmse":0.006141350604593754,"target_height":0.30850143536142827,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00020549038890749216,"lin_x_abs_mean":0.00725272111594677,"mean_actual_lin_x":-0.002465086057782173,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008215098641812801,"pitch_rate_abs_p99":0.1966637820005417,"pitch_rmse":0.0043594371527433395,"target_height":0.30850143536142827,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.00026068216538988054,"lin_x_abs_mean":0.007244644686579704,"mean_actual_lin_x":0.0020972939673811197,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.0075866589322686195,"pitch_rate_abs_p99":0.20680899918079376,"pitch_rmse":0.004231896251440048,"target_height":0.30850143536142827,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.00021906426991336048,"lin_x_abs_mean":0.009111982770264149,"mean_actual_lin_x":0.006999333389103413,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.009786408394575119,"pitch_rate_abs_p99":0.2177172303199768,"pitch_rmse":0.005188972223550081,"target_height":0.30850143536142827,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00013491036952473223,"lin_x_abs_mean":0.01271043997257948,"mean_actual_lin_x":0.011589261703193188,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.011163453571498394,"pitch_rate_abs_p99":0.25299277901649475,"pitch_rmse":0.006489579100161791,"target_height":0.30850143536142827,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0},{"height_rmse":0.00010744819155661389,"lin_x_abs_mean":0.008638516999781132,"mean_actual_lin_x":-0.0070896209217607975,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.011002922430634499,"pitch_rate_abs_p99":0.19213919341564178,"pitch_rmse":0.006156035698950291,"target_height":0.3145586657098365,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00020254874834790826,"lin_x_abs_mean":0.006960600148886442,"mean_actual_lin_x":-0.0026815468445420265,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008341909386217594,"pitch_rate_abs_p99":0.20080962777137756,"pitch_rmse":0.0043068393133580685,"target_height":0.3145586657098365,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.00027750778826884925,"lin_x_abs_mean":0.0071690804325044155,"mean_actual_lin_x":0.002367328153923154,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007725246716290712,"pitch_rate_abs_p99":0.19581986963748932,"pitch_rmse":0.004219655878841877,"target_height":0.3145586657098365,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.0002904982538893819,"lin_x_abs_mean":0.008898716419935226,"mean_actual_lin_x":0.006916059646755457,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.009638802148401737,"pitch_rate_abs_p99":0.2054133117198944,"pitch_rmse":0.0051255011931061745,"target_height":0.3145586657098365,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00019373034592717886,"lin_x_abs_mean":0.0122893201187253,"mean_actual_lin_x":0.011398443952202797,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.010842766612768173,"pitch_rate_abs_p99":0.22365739941596985,"pitch_rmse":0.006231054197996855,"target_height":0.3145586657098365,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0},{"height_rmse":0.00011218861618544906,"lin_x_abs_mean":0.008709180168807507,"mean_actual_lin_x":-0.007137898821383715,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.010955187492072582,"pitch_rate_abs_p99":0.1973436176776886,"pitch_rmse":0.0061577362939715385,"target_height":0.32061589605824475,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00016890361439436674,"lin_x_abs_mean":0.0069791697897017,"mean_actual_lin_x":-0.0024877001997083426,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008550627157092094,"pitch_rate_abs_p99":0.19760197401046753,"pitch_rmse":0.004442795645445585,"target_height":0.32061589605824475,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.00026882870588451624,"lin_x_abs_mean":0.006823875475674868,"mean_actual_lin_x":0.0015672380104660988,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007626565173268318,"pitch_rate_abs_p99":0.2056138664484024,"pitch_rmse":0.003999816719442606,"target_height":0.32061589605824475,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.00028351243236102164,"lin_x_abs_mean":0.008918791078031063,"mean_actual_lin_x":0.006937229540199041,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.00932585820555687,"pitch_rate_abs_p99":0.20580443739891052,"pitch_rmse":0.005009614862501621,"target_height":0.32061589605824475,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.00022225864813663065,"lin_x_abs_mean":0.012313591316342354,"mean_actual_lin_x":0.011227017268538475,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.011337549425661564,"pitch_rate_abs_p99":0.24478933215141296,"pitch_rmse":0.0066415490582585335,"target_height":0.32061589605824475,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0},{"height_rmse":0.0002104254817822948,"lin_x_abs_mean":0.009115445427596569,"mean_actual_lin_x":-0.007721322122961283,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.010264570824801922,"pitch_rate_abs_p99":0.18918564915657043,"pitch_rmse":0.0055488101206719875,"target_height":0.326673126406653,"target_pitch":-0.079140027919641,"terminated_events":0,"vx_command":0},{"height_rmse":0.00011169620847795159,"lin_x_abs_mean":0.006535099353641272,"mean_actual_lin_x":-0.0025435301940888166,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.008128964342176914,"pitch_rate_abs_p99":0.1946735382080078,"pitch_rmse":0.004189266823232174,"target_height":0.326673126406653,"target_pitch":-0.040354653665737504,"terminated_events":0,"vx_command":0},{"height_rmse":0.0002033898636000231,"lin_x_abs_mean":0.006897625979036093,"mean_actual_lin_x":0.0018619117327034473,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.007795293815433979,"pitch_rate_abs_p99":0.20958605408668518,"pitch_rmse":0.004247201606631279,"target_height":0.326673126406653,"target_pitch":-0.0015692794118340042,"terminated_events":0,"vx_command":0},{"height_rmse":0.00024582105106674135,"lin_x_abs_mean":0.008536030538380146,"mean_actual_lin_x":0.0066144876182079315,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.009855748154222965,"pitch_rate_abs_p99":0.19476854801177979,"pitch_rmse":0.005127625539898872,"target_height":0.326673126406653,"target_pitch":0.0372160948420695,"terminated_events":0,"vx_command":0},{"height_rmse":0.0002240820467704907,"lin_x_abs_mean":0.012142687104642391,"mean_actual_lin_x":0.011313319206237793,"non_wheel_contact_rate":0,"pitch_error_abs_p95":0.011474156752228737,"pitch_rate_abs_p99":0.20383119583129883,"pitch_rmse":0.00683866161853075,"target_height":0.326673126406653,"target_pitch":0.076001469095973,"terminated_events":0,"vx_command":0}],"latency_cells":[{"delay_ms":0,"delay_steps":0,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.011043879203498363,"policy":"zero_residual","post_kick_lin_x_abs_max":0.1307574063539505,"recovery_time_s":0.1,"standing_abs_vx_mean":0.006987220607697964,"terminated_events":0,"tracking_abs_error_mean":0.00720513891428709,"tracking_abs_error_p95":0.01852722093462944},{"delay_ms":20,"delay_steps":1,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.012163268402218819,"policy":"zero_residual","post_kick_lin_x_abs_max":0.11997531354427338,"recovery_time_s":0.18,"standing_abs_vx_mean":0.007109735161066055,"terminated_events":0,"tracking_abs_error_mean":0.008248977363109589,"tracking_abs_error_p95":0.020016200840473175},{"delay_ms":40,"delay_steps":2,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.013558503240346909,"policy":"zero_residual","post_kick_lin_x_abs_max":0.12098667770624161,"recovery_time_s":0.26,"standing_abs_vx_mean":0.008761467412114143,"terminated_events":0,"tracking_abs_error_mean":0.008709645830094814,"tracking_abs_error_p95":0.021766146644949913},{"delay_ms":60,"delay_steps":3,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.017446143552660942,"policy":"zero_residual","post_kick_lin_x_abs_max":0.13287465274333954,"recovery_time_s":0.4,"standing_abs_vx_mean":0.010456238873302937,"terminated_events":0,"tracking_abs_error_mean":0.0116716418415308,"tracking_abs_error_p95":0.027849527075886726},{"delay_ms":80,"delay_steps":4,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.02760768122971058,"policy":"zero_residual","post_kick_lin_x_abs_max":0.1461997777223587,"recovery_time_s":0.92,"standing_abs_vx_mean":0.01839355006814003,"terminated_events":0,"tracking_abs_error_mean":0.020391298457980156,"tracking_abs_error_p95":0.04236597567796707},{"delay_ms":0,"delay_steps":0,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.010844380594789982,"policy":"zero_residual","post_kick_lin_x_abs_max":0.11990196257829666,"recovery_time_s":0.08,"standing_abs_vx_mean":0.006949808448553085,"terminated_events":0,"tracking_abs_error_mean":0.007256990298628807,"tracking_abs_error_p95":0.01863228529691696},{"delay_ms":20,"delay_steps":1,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.011869456619024277,"policy":"zero_residual","post_kick_lin_x_abs_max":0.12309412658214569,"recovery_time_s":0.18,"standing_abs_vx_mean":0.007007367443293333,"terminated_events":0,"tracking_abs_error_mean":0.007992643862962723,"tracking_abs_error_p95":0.020468534901738167},{"delay_ms":40,"delay_steps":2,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.013673351146280766,"policy":"zero_residual","post_kick_lin_x_abs_max":0.12961448729038239,"recovery_time_s":0.28,"standing_abs_vx_mean":0.00862827431410551,"terminated_events":0,"tracking_abs_error_mean":0.009000776335597038,"tracking_abs_error_p95":0.022732291370630264},{"delay_ms":60,"delay_steps":3,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.017853394150733948,"policy":"zero_residual","post_kick_lin_x_abs_max":0.1293426901102066,"recovery_time_s":0.3,"standing_abs_vx_mean":0.010524452663958073,"terminated_events":0,"tracking_abs_error_mean":0.012121072970330715,"tracking_abs_error_p95":0.02783133089542389},{"delay_ms":80,"delay_steps":4,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.028069453313946724,"policy":"zero_residual","post_kick_lin_x_abs_max":0.150909423828125,"recovery_time_s":1.26,"standing_abs_vx_mean":0.018602658063173294,"terminated_events":0,"tracking_abs_error_mean":0.02049054391682148,"tracking_abs_error_p95":0.0429089218378067},{"delay_ms":0,"delay_steps":0,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.01314107608050108,"policy":"zero_residual","post_kick_lin_x_abs_max":0.1414753943681717,"recovery_time_s":0.18,"standing_abs_vx_mean":0.014406519010663033,"terminated_events":0,"tracking_abs_error_mean":0.014303396455943584,"tracking_abs_error_p95":0.038086310029029846},{"delay_ms":20,"delay_steps":1,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.014085836708545685,"policy":"zero_residual","post_kick_lin_x_abs_max":0.12586554884910583,"recovery_time_s":0.22,"standing_abs_vx_mean":0.014244974590837955,"terminated_events":0,"tracking_abs_error_mean":0.014384638518095016,"tracking_abs_error_p95":0.03695063665509224},{"delay_ms":40,"delay_steps":2,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.01747898943722248,"policy":"zero_residual","post_kick_lin_x_abs_max":0.1387210190296173,"recovery_time_s":0.28,"standing_abs_vx_mean":0.015932835638523102,"terminated_events":0,"tracking_abs_error_mean":0.015655843541026115,"tracking_abs_error_p95":0.04021057114005089},{"delay_ms":60,"delay_steps":3,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.021695401519536972,"policy":"zero_residual","post_kick_lin_x_abs_max":0.14992760121822357,"recovery_time_s":0.44,"standing_abs_vx_mean":0.017228471115231514,"terminated_events":0,"tracking_abs_error_mean":0.017300719395279884,"tracking_abs_error_p95":0.04270332679152489},{"delay_ms":80,"delay_steps":4,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.03229844570159912,"policy":"zero_residual","post_kick_lin_x_abs_max":0.20006190240383148,"recovery_time_s":1.34,"standing_abs_vx_mean":0.02235904522240162,"terminated_events":1,"tracking_abs_error_mean":0.02192194014787674,"tracking_abs_error_p95":0.0547175295650959},{"delay_ms":0,"delay_steps":0,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.020785534754395485,"policy":"zero_residual","post_kick_lin_x_abs_max":0.1483522653579712,"recovery_time_s":0.34,"standing_abs_vx_mean":0.02334274724125862,"terminated_events":0,"tracking_abs_error_mean":0.02241542376577854,"tracking_abs_error_p95":0.054450251162052155},{"delay_ms":20,"delay_steps":1,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.02451029047369957,"policy":"zero_residual","post_kick_lin_x_abs_max":0.1624964475631714,"recovery_time_s":0.44,"standing_abs_vx_mean":0.025096632540225983,"terminated_events":0,"tracking_abs_error_mean":0.02479550987482071,"tracking_abs_error_p95":0.06114121526479721},{"delay_ms":40,"delay_steps":2,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.03026701882481575,"policy":"zero_residual","post_kick_lin_x_abs_max":0.1623184084892273,"recovery_time_s":0.56,"standing_abs_vx_mean":0.027675826102495193,"terminated_events":0,"tracking_abs_error_mean":0.02679629996418953,"tracking_abs_error_p95":0.06524382531642914},{"delay_ms":60,"delay_steps":3,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.038258396089076996,"policy":"zero_residual","post_kick_lin_x_abs_max":0.17828451097011566,"recovery_time_s":0.74,"standing_abs_vx_mean":0.0303372610360384,"terminated_events":0,"tracking_abs_error_mean":0.02987164817750454,"tracking_abs_error_p95":0.07334631681442261},{"delay_ms":80,"delay_steps":4,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.0708014965057373,"policy":"zero_residual","post_kick_lin_x_abs_max":0.2983553111553192,"recovery_time_s":3.58,"standing_abs_vx_mean":0.04753377288579941,"terminated_events":2,"tracking_abs_error_mean":0.04053782299160957,"tracking_abs_error_p95":0.10227109491825104},{"delay_ms":0,"delay_steps":0,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.011351809836924076,"policy":"candidate","post_kick_lin_x_abs_max":0.11191771924495697,"recovery_time_s":0.08,"standing_abs_vx_mean":0.006497347727417946,"terminated_events":0,"tracking_abs_error_mean":0.006531170569360256,"tracking_abs_error_p95":0.01671610213816166},{"delay_ms":20,"delay_steps":1,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.011603688821196556,"policy":"candidate","post_kick_lin_x_abs_max":0.14142851531505585,"recovery_time_s":0.22,"standing_abs_vx_mean":0.00858239084482193,"terminated_events":0,"tracking_abs_error_mean":0.008699791505932808,"tracking_abs_error_p95":0.021975353360176086},{"delay_ms":40,"delay_steps":2,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.013165956363081932,"policy":"candidate","post_kick_lin_x_abs_max":0.12976570427417755,"recovery_time_s":0.24,"standing_abs_vx_mean":0.009301927872002125,"terminated_events":0,"tracking_abs_error_mean":0.01005501952022314,"tracking_abs_error_p95":0.02599981613457203},{"delay_ms":60,"delay_steps":3,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.016171107068657875,"policy":"candidate","post_kick_lin_x_abs_max":0.132547527551651,"recovery_time_s":0.3,"standing_abs_vx_mean":0.010480305179953575,"terminated_events":2,"tracking_abs_error_mean":0.011140689253807068,"tracking_abs_error_p95":0.027021288871765137},{"delay_ms":80,"delay_steps":4,"kick_event_count":64,"noise_tier":"none","non_wheel_contact_rate":0,"pitch_abs_p95":0.030529405921697617,"policy":"candidate","post_kick_lin_x_abs_max":0.2935265600681305,"recovery_time_s":2.1,"standing_abs_vx_mean":0.019155452027916908,"terminated_events":6,"tracking_abs_error_mean":0.020555447787046432,"tracking_abs_error_p95":0.04886236786842346},{"delay_ms":0,"delay_steps":0,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.011157880537211895,"policy":"candidate","post_kick_lin_x_abs_max":0.11497818678617477,"recovery_time_s":0.08,"standing_abs_vx_mean":0.006153447553515434,"terminated_events":0,"tracking_abs_error_mean":0.006454714108258486,"tracking_abs_error_p95":0.016684992238879204},{"delay_ms":20,"delay_steps":1,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.011300064623355865,"policy":"candidate","post_kick_lin_x_abs_max":0.12796908617019653,"recovery_time_s":0.16,"standing_abs_vx_mean":0.008384688757359982,"terminated_events":0,"tracking_abs_error_mean":0.008600873872637749,"tracking_abs_error_p95":0.022157354280352592},{"delay_ms":40,"delay_steps":2,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.013002783991396427,"policy":"candidate","post_kick_lin_x_abs_max":0.13947659730911255,"recovery_time_s":0.24,"standing_abs_vx_mean":0.009780127555131912,"terminated_events":0,"tracking_abs_error_mean":0.009976571425795555,"tracking_abs_error_p95":0.02580813691020012},{"delay_ms":60,"delay_steps":3,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.01647009328007698,"policy":"candidate","post_kick_lin_x_abs_max":0.13268159329891205,"recovery_time_s":0.36,"standing_abs_vx_mean":0.010261217132210732,"terminated_events":0,"tracking_abs_error_mean":0.011237612925469875,"tracking_abs_error_p95":0.027789568528532982},{"delay_ms":80,"delay_steps":4,"kick_event_count":64,"noise_tier":"encoder","non_wheel_contact_rate":0,"pitch_abs_p95":0.02985461615025997,"policy":"candidate","post_kick_lin_x_abs_max":0.15648983418941498,"recovery_time_s":1.18,"standing_abs_vx_mean":0.02020798623561859,"terminated_events":3,"tracking_abs_error_mean":0.019325407221913338,"tracking_abs_error_p95":0.045518577098846436},{"delay_ms":0,"delay_steps":0,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.01311526820063591,"policy":"candidate","post_kick_lin_x_abs_max":0.11053044348955154,"recovery_time_s":0.1,"standing_abs_vx_mean":0.013527307659387589,"terminated_events":0,"tracking_abs_error_mean":0.013584049418568611,"tracking_abs_error_p95":0.03556500002741814},{"delay_ms":20,"delay_steps":1,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.015923790633678436,"policy":"candidate","post_kick_lin_x_abs_max":0.14582562446594238,"recovery_time_s":0.26,"standing_abs_vx_mean":0.016116809099912643,"terminated_events":0,"tracking_abs_error_mean":0.015706516802310944,"tracking_abs_error_p95":0.04001062363386154},{"delay_ms":40,"delay_steps":2,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.019215052947402,"policy":"candidate","post_kick_lin_x_abs_max":0.15189579129219055,"recovery_time_s":0.3,"standing_abs_vx_mean":0.016692815348505974,"terminated_events":0,"tracking_abs_error_mean":0.016871217638254166,"tracking_abs_error_p95":0.04197467118501663},{"delay_ms":60,"delay_steps":3,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.02352210506796837,"policy":"candidate","post_kick_lin_x_abs_max":0.1679765284061432,"recovery_time_s":0.52,"standing_abs_vx_mean":0.018342306837439537,"terminated_events":0,"tracking_abs_error_mean":0.018747352063655853,"tracking_abs_error_p95":0.0467117503285408},{"delay_ms":80,"delay_steps":4,"kick_event_count":64,"noise_tier":"mems_imu","non_wheel_contact_rate":0,"pitch_abs_p95":0.0492582730948925,"policy":"candidate","post_kick_lin_x_abs_max":0.2198176383972168,"recovery_time_s":1.66,"standing_abs_vx_mean":0.0349641889333725,"terminated_events":10,"tracking_abs_error_mean":0.028445031493902206,"tracking_abs_error_p95":0.07210559397935867},{"delay_ms":0,"delay_steps":0,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.020040947943925858,"policy":"candidate","post_kick_lin_x_abs_max":0.14655670523643494,"recovery_time_s":0.14,"standing_abs_vx_mean":0.022375021129846573,"terminated_events":0,"tracking_abs_error_mean":0.022285910323262215,"tracking_abs_error_p95":0.053159549832344055},{"delay_ms":20,"delay_steps":1,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.026711465790867805,"policy":"candidate","post_kick_lin_x_abs_max":0.157490074634552,"recovery_time_s":0.36,"standing_abs_vx_mean":0.025624293833971024,"terminated_events":0,"tracking_abs_error_mean":0.025862382724881172,"tracking_abs_error_p95":0.06469564884901047},{"delay_ms":40,"delay_steps":2,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.03461362048983574,"policy":"candidate","post_kick_lin_x_abs_max":0.20025943219661713,"recovery_time_s":0.56,"standing_abs_vx_mean":0.029068009927868843,"terminated_events":0,"tracking_abs_error_mean":0.02860417775809765,"tracking_abs_error_p95":0.07147517055273056},{"delay_ms":60,"delay_steps":3,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.043304260820150375,"policy":"candidate","post_kick_lin_x_abs_max":0.1822700798511505,"recovery_time_s":0.62,"standing_abs_vx_mean":0.0323825441300869,"terminated_events":0,"tracking_abs_error_mean":0.03217266872525215,"tracking_abs_error_p95":0.07953979820013046},{"delay_ms":80,"delay_steps":4,"kick_event_count":64,"noise_tier":"mems_imu_2x","non_wheel_contact_rate":0,"pitch_abs_p95":0.12649685144424438,"policy":"candidate","post_kick_lin_x_abs_max":1.6340394020080566,"recovery_time_s":5.04,"standing_abs_vx_mean":0.07934746146202087,"terminated_events":22,"tracking_abs_error_mean":0.06326030939817429,"tracking_abs_error_p95":0.16573189198970795}],"interface":{"policy":"clip(raw, -1, 1) -> mask -> scale","wheels":"classical + mapped balance/yaw residual -> slew limit -> velocity clip","legs":"posture map + four leg residuals -> soft joint-position clip -> encoder bias correction","outputs":["2 wheel velocity targets (rad/s)","4 leg position targets (rad)"],"posture_reference":"height/pitch slew is upstream; no separate final leg slew in this historical action implementation"}}